## Slide 1: STRX CALIBRATION API
NOVEMBER 2021
Maxim Kulesh, Artur Burchard

## Slide 2: RFE SW: Dynamic View of Radar System Cycle
Radar Cycle
[1ms]
Init
FIT
Start up Calib.
Radar Config
Config. Calib.
Safety Timeslot
Sensor
Idle
Acquisition
(Re-) Calib.
Startup
Customer initiates radar re-configuration
Idle
Idle

## Slide 3: Smarttrx Start-Up calibration items
STRX Start-up Calibration | Time [us]
ATB ADC Start-up Calibration | 1000
RX ADC Start-up Re-Calibration | 300
Total Time | 1300

## Slide 4: Smarttrx Configuration calibration itemS
STRX Profile Independent Configuration Calibration | Time [us] (simulated)
LOI Tx Buffer Calibration | 120
LOI Rx Buffer Calibration | 90
TX LOX2 Calibration | 110
TX Buff2a Calibration | 130
TX Buff2b2c Calibration | 130
TX PR Calibration | 855
RX LOX2 Calibration | 150
RFBIST LOX2 Calibration | 85
RFBIST SSB Calibration | 150
Total Time | 1820
STRX_SYS_ReadTempSensor (x4) | 80
STRX Profile Dependent Configuration Calibration | Time [us]
RX HPF Calibration (per profile) | 3200
RX Gain Calibration (per profile) | 700
RX LPF Calibration (per profile) | 465
ChirpPLL AAFC Calibration (per profile) | 200
TX Pout Calibration (per profile) | 530
Total Time (per profile) | 5095
To calculate the duration of configuration calibration phase the following shall be used:
total time = [profile independent calibrations] +
[profile dependent calibrations] * [number of profiles used]

## Slide 5: Smarttrx calibration items
STRX Profile Independent Calibration | ReCalibration (Config Calib) [us] | Recalibration* (optimized) [us]
STRX_LOI_TxBufferCalibration | 120 | 75
STRX_LOI_RxBufferCalibration | 90 | 60
STRX_TX_LOX2Calibration | 110 | 65
STRX_TX_Buff2aCalibration | 130 | 65
STRX_TX_Buff2b2cCalibration | 130 | 65
STRX_TX_PRCalibration | 855 | 600
STRX_RX_LOX2Calibration | 110 | 65
STRX_RFBIST_LOX2Calibration | 85 | 55
STRX_RFBIST_SSBCalibration | 110 | 55
STRX_SYS_ReadTempSensor (x4) | 80 | 80
STRX Profile Dependent Calibration | ReCalibration (simulated) [us] | Recalibration* (optimized) [us]
STRX_ChirpPLL_AAFC (per profile) | 200 | 200
STRX_TX_PoutCalibration (per profile) | 530 | 300
Total | 2550 | 1685
* Note: Optimised Calibration will be available June 2022 EAR 1.4, for the rest of the document we use simulated data
To calculate the duration of re-calibration phase per chirp sequence[x] the following shall be used:
total time[x] = [profile independent re-calibrations] * [recalibrateProfileIndependent] +
[profile dependent re-calibrations] * [recalibrateProfileDependent[x]]
so taking into account RFE calibrations settings per given chirp sequence:
recalibrateProfileDependent[x]
recalibrateProfileIndependent

## Slide 6: CALIBRATION CONFIGURATION / API
idle
Chirp Sequence 1
Single radar frame / system cycle could consist of multiple chirp sequences (LR / MR)
Calibration slot can be configured before any chirp sequence:
  Calibration slot can be configured to perform profile independent calibrations
  Calibration slot can be configured to perform profile dependent calibrations (AAFC, Pout)
  Calibration slot is not limited to profiles used in subsequent chirp sequence only, i.e. calibration slot 1 can include profiles from chirp sequence 2.
Cal 1
Chirp Sequence 2
Cal 2
BIST
idle
Profile Independent calibrations: yes / no
Profile Dependent Calibrations
Profile 1: yes / no
Profile 2: yes / no
Profile 3: yes / no
Profile 4: yes / no
…
Profile 8: yes / no
Profile Independent calibrations: yes / no
Profile Dependent Calibrations
Profile 1: yes / no
Profile 2: yes / no
Profile 3: yes / no
Profile 4: yes / no
…
Profile 8: yes / no

## Slide 7: CALIBRATION CONFIGURATION / API EXAMPLES
idle
Chirp Sequence 1 / LR
Cal 1
Chirp Sequence 2 / MR
Cal 2
BIST
idle
a)
Profile Independent calibrations: Yes
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: Yes
- all used profiles for Chirp Sequence 2: No
50ms
idle
Chirp Sequence 1 / LR
Cal 1
Chirp Sequence 2 / MR
Cal 2
BIST
idle
b)
50ms
Idle
idle
Chirp Sequence 1 / LR
Cal 1\2
Chirp Sequence 2 / MR
BIST
idle
c)
idle
50ms
Profile Independent calibrations: Yes
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: No
- all used profiles for Chirp Sequence 2: Yes
Profile Independent calibrations: Yes
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: Yes
- all used profiles for Chirp Sequence 2: No
Profile Independent calibrations: No
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: No
- all used profiles for Chirp Sequence 2: Yes
Profile Independent calibrations: Yes
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: Yes
- all used profiles for Chirp Sequence 2: Yes
Profile Independent calibrations: No
Profile Dependent calibrations:
- all used profiles for Chirp Sequence 1: No
- all used profiles for Chirp Sequence 2: No

## Slide 8: CALIBRATION CONFIGURATION / EXAMPLE B (DENSO)
idle
Chirp Sequence 1 / LR
Cal 1
Chirp Sequence 2 / MR
Cal 2
BIST
idle
b)
Duration: 2550 us
Duration: 200/730*us
50ms
STRX_LOI_TxBufferCalibration
STRX_LOI_RxBufferCalibration
STRX_TX_LOX2Calibration
STRX_TX_Buff2aCalibration
STRX_TX_Buff2b2cCalibration
STRX_TX_PRCalibration
STRX_RX_LOX2Calibration
STRX_RFBIST_LOX2Calibration
STRX_RFBIST_SSBCalibration
STRX_SYS_ReadTempSensor (x4)
STRX_ChirpPLL_AAFC - Profile : LR
STRX_TX_PoutCalibration - Profile : LR
Bist Duration:
Target = < 2 ms
STRX_ChirpPLL_AAFC - Profile : MR
STRX_TX_PoutCalibration - Profile : MR
(*) P_out calibration (530[us]) for MR is needed only if power is different then LR