## Slide 1: ARM M7 SIMD & FPU programing Introduction
17th May 2021
Hong Li
hong.r.li@nxp.com

## Slide 2: STRX RFE Cortex-M7 SIMD & FPU programming
A Cortex-M7 DSP in STRX-RFE for RFE control
  FW of STRX-RFE HW control & API for costumer to run STRX-RFE
    Configure STRX-RFE modes with full RFE registers access to control STRX RFE
    Calibrate STRX-RFE on different working modes and chirp modes in runtime
  STRX-RFE chip test FW for DfT support
    Test STRX in chip production testing
  Calibration and DfT testing requires signal processing functions
    FFT, DFT, SQRT, Log10/Log2, Atan/Angle…  M7 DSP math library
Cortex-M7 computing capability
  DPU: Normal 32-bit arithmetic, 2x16bit and 4x8-bit SIMD
    Fast 2x16bit SIMD instructions, e.g. Mul+Add/Sub…
  FPU: Single-precision floating-point high accuracy arithmetic
    Adv. FPU instructions, e.g. Mul+Add/Sub, SQRT…
  M7: 160MHz + 32kB RAM + 3.5MB (slower) shared memory

## Slide 3: Math function Requirements from STRX Calibration and Chip test
FFT: real and complex input
  Size up to 16k, In-place processing, requires log absolute amplitude accuracy 0.1dB or 1.16% and angle accuracy 0.05 deg
  Real single-bit input FFT size up to 2^19, with the same accuracy as normal real input FFT
DFT: single-bin and dual-bin DFT on real input
  Size up to requires amplitude accuracy 0.1dB or 1.16% and angle accuracy 0.05 deg
Square-Root sqrt: accuracy better than 1.16%
Log10 / log2: accuracy better than 1.16%
Atan / phase / angle: accuracy better than 0.05 deg
Mean / std / Max / Min
Complex data power / Abs: accuracy better than 1.16%
Histogram
Sorting
Polynomial: Order-3 polynomial a0+ a1*v1 + a2*v2 +a3*v3, requires floating-point accuracy
TBD following progress of teams on DfT, Calibration and Bist, etc.

## Slide 4: FFT spectrum phase/ complex number angle accuracy analysis
For a given relative error in x, i.e. Rerrx, max Atan(x) error at x~1
  Angle error < 0.3 ° if Rerrx < %1 (0.1dB  1.16%)
    when x has 7 mantissa bits
  Angle error < 0.6° if Rerrx < 2%
    When x has 6 mantissa bits
  Angle error < 0.6° for a complex number with 1% relative error in real and imaginary parts, and 6 mantissa bits
    For a complex number with relative error ε in real and imaginary parts, its Rerrx < 2 ε
FFT spectrum phase error < 0.05 ° requires
  FFT spectrum I and Q relative error < 1e-3 (0.0087dB)
  Need floating-point FFT calculation or 32-bit integer calculation (no SIMD intrinsic gain)

## Slide 5: Enable M7 SIMD programming using ARM Open source CMSIS-CORE headers
CMSIS-core has defined SIMD intrinsic,
  Better use ARM compiler 6.16 with a lot intrinsic built in compiler library
  Intrinsic Functions for SIMD Instructions [only Cortex-M4 and Cortex-M7] (keil.com)
  Need to edit DEVICE.h to eg. strxm7_Device.h with STRX-M7 capability in M3SA
    In m3sa\eclipse-cpp-2020-09-R-win32-x86_64\eclipse\plugins\ilg.gnumcueclipse.templates.cortexm_1.5.2.202010292017\templates\cortexm_project\Vendor\DEVICE\include\
    Include <core_cm7.h> for __ARM_ARCH_7EM__ architecture
    Define __CM7_REV as 0x0102
    Define __FPU_PRESENT and __MPU_PRESENT as 1
    IRQn, memory map, IQ map …?
    2nd DPU?
  Include this “strxm7_Device.h” and <core_cmSimd.h> in your system root header file to enable SIMD compiling using CMSIS-core headers
  Note: CMSIS document is as bad as ( worse than ) BBE
    Confusing & wrong virtual code
    Missing cycle counts and exceptions

## Slide 6: SIMD Instruction and flag register OVERVIEW
63 SIMD intrinsic instructions
  Arithmetic instructions for 1x32-bit / 2x16bit / 4x8bit data
39 CPU instructions
  Load, store, rotate/saturate value, IRQ/event
xPSR/APSR core Program Status Register used by SIMD instructions
  xPSR includes IRQ and arithmetic flags
  APSR includes only arithmetic flags
    Same as in flags in xPSR
    Q:
      Saturation-flag of QADD/QSUB/Q..
      Overflow flag in SMLADx mul-accumu instructions
      Sticky flag: Need to define a new intrinsic to call msr to reset  Occasionally check, maybe? useful for calculation safety check
    GE[3:0]:
      select-indi of SEL,
      sign-flag of SADD/SSUB/S… and UADD/USUB/U…
    N: not used in SIMD?
    …
typedef union
{
struct {/*!< Structure used for bit access */
uint32_t ISR:9; /*!< bit: 0.. 8 Exception number */
uint32_t _reserved0:7; /*!< bit: 9..15 Reserved */
uint32_t GE:4; /*!< bit: 16..19 Greater than or Equal flags */
uint32_t _reserved1:4; /*!< bit: 20..23 Reserved */
uint32_t T:1; /*!< bit: 24 Thumb bit (read 0) */
uint32_t IT:2; /*!< bit: 25..26 saved IT state (read 0) */
uint32_t Q:1; /*!< bit: 27 Saturation condition flag */
uint32_t V:1; /*!< bit: 28 Overflow condition flag */
uint32_t C:1; /*!< bit: 29 Carry condition flag */
uint32_t Z:1; /*!< bit: 30 Zero condition flag */
uint32_t N:1; /*!< bit: 31 Negative condition flag */
} b;
uint32_t w; /*!< Type used for word access */
} xPSR_Type;

## Slide 7: SIMD intrinsic Summary – 45 instructions for ADD/SUB 2x16bit/ 4X8Bit data
12 full resolution ADD, SUB and exchanged ADD-SUB, with sign bit in APSR.GE[3:0]
  Signed data SADD16 / SSUB16, SADD8 / SSUB8 and SSAX / SASX, GE bit set to 1, if result >= 0
  Unsigned data UADD16 / USUB16, UADD8 / USUB8 and USAX / UASX, GE bit set to 1, if sum overflows or diff>=0
14 Saturated ADD, SUB and exchanged ADD-SUB
  Signed data QADD / QSUB, QADD16 / QSUB16, QADD8 / QSUB8 and QASX / QSAX, with APSR.Q bit set to 1, if saturated
    Saturated to [-231, 231-1] / [-215, 215-1] / [-27, 27-1], respectively
  Unsigned UQADD16 / UQADD8, UQSUB16 / UQSUB8 and UQASX / UQSAX, saturated to [0, 216-1] / [0, 28-1], but no touch to APSR.Q
12 Halved ADD, SUB and exchanged ADD-SUB, with results right-shifted by 1 (>>1)
  Signed data SHADD16 / SHSUB16, SHADD8 / SHSUB8 and SHSAX / SHASX, with results in range [-215, 215-1] / [-27, 27-1]
  Unsigned data UHADD16 / UHSUB16, UADD8 / USUB8 and UHSAX / UHASX,
    Sum range [0, 216-1] / [0, 28-1], but diff range [-215, 215-1] / [-27, 27-1]
7 intrinsic for 8-bit value extraction and accumulation
  Uint32_t SXTB16(uint32_t v1) / UXTB16(uint32_t v1) exTracts the low byte of each 16-bit word, Signed/Unsigned-eXtends and returns it as 16-bit word
  SXTAB16 / UXTAB16 accumulates the 1st input with the extended the low byte (as SXTB/UXTB) of the 2nd input, then returns accumulated two words.
    If accumulation overflows, it just returns uint16_t casted value  Need programmer to prevent overflow by limiting the 1st input
  SXTB16_RORn (SXTB16 with input byte-rotation) is missing in CMSIS-Core 2016
  USAD8 / USADA8 unsigned-accumulates 4 absolute byte-differences between the two inputs and returns the accumulation.
    If USADA8 overflows (due to sum to the 3rd uint32_t input), it just returns uint32_t casted value and ignores the carrier  Programmer can find carrier by the result and the 3rd input
2 Saturation: SSAT16 / USAT16 saturates value to a given bit size (must be instant value in source code)
  Signed saturation SSAT16 cannot saturate a negative value to zero, because (-1)>>n = -1 in arithmetic right shift!
Res = __SASX(v1,v2)
Signed
1st ADD:
v1H+v2L
2nd SUB:
v1L+v2H
H-L eXchanged
Res = __USAX(v1,v2)
Unsigned
1st SUB:
v1H-v2L
2nd ADD:
v1L+v2H
H-L eXchanged

## Slide 8: SIMD intrinsic Summary – 13 Signed-Multiply for 2x16bit/ 4X8Bit data
4 full-resolution 2x16bit Multiply and ADD/SUB int64_t products, then accumulate to the 3rd int64_t value
  Signed data SMLALD / SMLSLD, SMLALDX / SMLSLDX, w/o input word eXchange
  if accumulation overflows, it returns 264 modulo:  Need programmer to prevent overflow by limiting v3
    Uint64_t __SMLALD(uint32_t v1, uint32_t v2, uint64_t v3): p1= (int16_t)v1H * (int16_t)v2H; p1= (int16_t)v1L * (int16_t)v2L;
    res64 = ( p1 + p2 + (int64_t)v3 ) % 264
4 2x16bit Multiply and ADD/SUB int32_t products, then accumulate to 3rd int32_t input, with APSR.Q set to 1, if overflows
  SMLAD / SMLSD, SMLADX / SMLSDX, w/o input word exchange
  if accumulation overflows, it returns (uint32_t) casted value  Need programmer to prevent overflow
4 2x16bit Multiply and ADD/SUB int32_t products, returns the product sum/difference
  SMUAD / SMUSD and SMUADX / SMUSDX, w/o input word exchange
  No overflow in SMUSDX and SMUSD, while SMUAD and SMUADX overflows only when the two inputs are all 0x80008000 with APSR.Q set to 1
1 intrinsic for accumulation of the 3rd input and the high-32bit of 32bit signed-multiply product of the first two inputs
  Uint32_t SMMLA(uint32_t v1, uint32_t v2, uint32_t v3) = ((int32_t)v1 * (int32_t)v2)>>32 + (int32_t)v3
  If accumulation overflow, it just returns (uint32_t) casted value  Need programmer to prevent overflow by limiting v3 value
Res = __SMLALDX(v1,v2,v3)
Signed X
ADD prod
Long porD
H-L eXchanged
Res = __SMLSDX(v1,v2,v3)
Signed X
SUB proDd
H-L eXchanged

## Slide 9: Enable M7 FPU programming
Compiling options
  Options for FPU hardware: -mfloat-abi=hard -mfpu=fpv5-sp-d16
  Armclang compiler needs also linker option: --fpu=FPv5-SP
Need to enable FPU
  /* Enable FPU */
  __STATIC_INLINE void rfeDsp_enableFPU ( void ) { /* Enable FPU */
  *( ( volatile uint32_t* )0xE000ED88 ) |= 0xful << 20ul ;
  __DSB(); // _dsb();
  __ISB(); // _isb();
  }
No FPU intrinsic defined in ARM CMSIS Open-Source community
  May need to define our own for optimization, currently just compiling on normal C code
Recommend to use type casting to do integer-float conversion
Recommend to put ‘F’ after each float constant in source, to confirm single-precision floating point value
  Such as float v1 = 0.01F;

## Slide 10: FPU Instruction and flag register OVERVIEW
38 FPU instructions on 32 FPU registers
  3 Load, 3 store, 2 push/pop
  12 float-double-integer conversion
  9 floating-point arithmetic instructions:
    div, mul, add, sub, mul-add/sub, neg-mul-add/sub
  1 MOV, 2 Max/min, 1 SEL, 1 ABS, 1 NEG, 1 SQRT, 2 CMP
FPSCR FPU Status Register
  4 (2-bit) Rounding modes
  6 exception flags
  4-bit float comparison flags
  1-bit NaN mode control
  1-bit Flush to zero mode control
typedef union {
struct { /*!< Structure used for bit access */
uint32_t IOC:1; /*!< bit: 0 Invalid operation cumulative exception bit */
uint32_t DZC:1; /*!< bit: 1 Divided by zero cumulative exception bit */
uint32_t OFC:1; /*!< bit: 2 Overflow cumulative exception bit */
uint32_t UFC:1; /*!< bit: 3 Underflow cumulative exception bit */
uint32_t IXC:1; /*!< bit: 4 Inexact cumulative exception bit */
uint32_t IDC:1; /*!< bit: 7 Input Denormal cumulative exception bit */
uint32_t RMode:2; /*!< bit: 22..23 Rounding mode: 00 nearest, 01 RM, 10 RP, 11 RZ */
uint32_t FZ:1; /*!< bit: 24 Flush-to-zero mode */
uint32_t DN:1; /*!< bit: 25 DN NaN mode control */
uint32_t AHP:1; /*!< bit: 26 Half-precision flag */
uint32_t V:1; /*!< bit: 28 Overflow condition flag, float compare */
uint32_t C:1; /*!< bit: 29 Carry condition flag, float compare */
uint32_t Z:1; /*!< bit: 30 Zero condition flag, float compare */
uint32_t N:1; /*!< bit: 31 Negative condition flag, float compare */
} b;
uint32_t w; /*!< Type used for word access */
} FPSCR_Type;

## Slide 11: Intrinsic Example of using FPU Instruction
/**
\brief __VSQRT float square-root
\details Returns square-root of a float value.
\param [in] sf The input float value.
\return result The square-root of the input value.
*/
__attribute__( ( always_inline ) ) __STATIC_INLINE float __VSQRT( float sf )
{
float result;
__ASM volatile ( "VSQRT.F32 %0, %1" : "=t" (result) : "t" (sf) );
return result;
}
/**
\brief __VABS float absolute
\details Return absolute value of a float value.
\param [in] sf The input float value.
\return result The absolute of the input value.
*/
__attribute__( ( always_inline ) ) __STATIC_INLINE float __VABS( float sf )
{
float result;
__ASM volatile ( "VABS.F32 %0, %1" : "=t" (result) : "t" (sf) );
return result;
}
Both Float casting and CVCT instructions can convert between integer and float
  Integer zero is converted to -0.0F
CVCT instruction group supports conversion between Q31/15. and float,
  But only with immediate / hard coded constant number of fraction bits
  Immediate / hard-coded number of fractional bits needed for Q31.n to float conversion
    Number of fractional bits for __CVCT_Q31.n2F(int32_t val, #nfBits) must be in [1, 32], but 32 is invalid for Q31.n
    __CVCT_Q31.n2F ( MIN_INT32_VAL, 32)  infinite

## Slide 12: Current results
Compiler issues solved for using SIMD and using FPU instructions
70% M7 DSP math library implementation completed
  Float-Q31/15.n conversion, SQRT & complex ABS, polynomial, min/max/mean/std, sorting, One-bin / dual-bin real input DFT
  IMD and FPU real input FFT: FPU FFT is about 1.5x slower than SIMD FFT ( FPU FFT maybe more optimized )
    Shared memory FFT is ~2x slower
  In progress (Marinus)
    Log2 & log 10
    Arctan / Angle
  To be implemented:
    Single-bit input FFT: just need bit-int16_t conversion + SIMD FFT
    Complex input FFT and Histogram
  Further math function speed optimization only if really required by DfT or calibration teams
M7 programming issues
  Intrinsic definition for using FPU mul+add/sub…
  Intrinsic definition for 4 advanced SIMD instructions
  Program State register usage and reset, e.g. APSR.Q reset, FPU FPSCR usage for divided by zero, conversion saturation, etc.
Armclang FFT size | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384
SIMD FFT cycles | 260 | 481 | 951 | 1870 | 3845 | 8035 | 16396 | 36173 |  |  |  | 
on shared-mem |  |  |  |  |  |  |  | 64124 | 138538 | 298013 | 639766 | 1362057
FPU FFT cycles | 386 | 713 | 1293 | 2557 | 5359 | 11473 | 24377 | 55226 |  |  |  | 
on shared-mem |  |  |  |  |  |  |  | 96797 | 212755 | 462717 | 998549 | 2139391

## Slide 13: M7-DSP 63 SIMD Intrinsic Instructions in CMSIS-Core

## Slide 14: Pack data from 2 inputs and saturate data (5) Instructions: Function Tested
PKHBT / PKHTB: Form data from two inputs with left/right shift of the 2nd input before pick a halfword
  uint32_t res = __PKHBT(uint32_t v1, uint32_t v2, immediate uint32_t I3): res[15:0] = val1[15:0];
    res[31:16] = (val2<<I3)[31:16]
  uint32_t res = __PKHTB(uint32_t v1, uint32_t v2, immediate uint32_t I3): res[31:16] = v1[31:16];
    res[15:0] = (((int32_t)v2)>>I3)[15:0]; /* undefined if I3>32 */
SEL: Form data from two inputs according to xPSR/APSR.GE[3:0]
  uint32_t res= __SEL(uint32_t v1, uint32_t v2): res32[31:24] = (APSR.GE[3]==1)? v1[31:24] : V2[31:24]; res32[23:16] = (APSR.GE[2]==1)? v1[23:16] : V2[23:16];
    res32[15:8] = (APSR.GE[1]==1)? v1[15:8] : V2[15:8]; res32[7:0] = (APSR.GE[0]==1)? v1[7:0] : V2[7:0];
SSAT16 / USAT16 signed/unsigned saturates 2x16bit signed data by a given bit size (must be immediate value in source code)
  uint32_t res= __SSAT16(uint32_t v1, immediate uint32_t I2): I2 must be in [1,16], saturate to range [(-32768)>>(16-I2), 32767>>(16-I2)];
  res[31, 16] = sat_I2((int16_t) v1[31,16]); res[15, 0] = sat_I2((int16_t) v1[15, 0]);
    SSAT16 cannot saturate a negative value to zero, because (-1)>>n = -1 in arithmetic right shift!
  uint32_t res= __USAT16(uint32_t v1, immediate uint32_t I2): I2 must be in [0,15], saturate to range [0, 32767>>(15-I2)];
  res[31, 16] = uSat_I2((int16_t) v1[31,16]); res[15, 0] = uSat_I2((int16_t) v1[15, 0]);
CMSIS online document issues: Operation virtual code not as clear as above
  All operation virtual codes miss sign-casting of the input data
  PKHTB and PKHBT operation code ‘res[31:16]=val2[31:16]<<I3’ is wrong, should be (val2<<I3)[31:16]
  PKHTB and PKHBT descriptions miss the requirement that the 3rd input must be instant value
  !!! PKHTB instruction returns strange number if the 3rd input (shift number) is larger than 32  need to check HW implementation?

## Slide 15: Signed Multiply and sum/diff products (5) instructions – Function Tested OK
SMUAD / SMUADX: Add products of 2x16bit signed data w/o eXchange. If overflow (only if v1=v2=0x80008000), xPSR/APSR.Q=1
  uint32_t res32 = __SMUAD (uint32_t v1, uint32_t v2): res32 = (uint32_t)(p1 + p2);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[31:16];
  uint32_t res32 = __SMUADX (uint32_t v1, uint32_t v2): res32 = (uint32_t)(p1 + p2);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
SMUSD / SMUSDX: Sub products of 2x16bit signed data w/o eXchange. Overflow impossible
  uint32_t res32 = __SMUSD (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)(p1 - p2);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) + (int16_t)v2[31:16];
  uint32_t res32 = __SMUSDX (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)(p1 - p2);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
SMLAD / SMLADX: Add 3rd input and products of 2x16bit signed data w/o eXchange. If overflow, APSR.Q=1, return uint32_t casted
  Need programmer to prevent overflow
  uint32_t res32 = __SMLAD (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)(p1+p2+(int32_t)v3);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) + (int16_t)v2[31:16];
  uint32_t res32 = __SMLADX (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)(p1+p2+(int32_t)v3);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
CMSIS online document issues: All operation virtual codes miss sign-casting of the input data

## Slide 16: Signed Multiply & Accumulation (8) instructions – Function Tested OK
SMLSD / SMLSDX: Sum 3rd input and product difference of 2x16bit (eXchanged) signed data. If overflow, xPSR/APSR.Q=1, return uint32_t casted
  uint32_t res32 = __SMLSD (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)(p1-p2+(int32_t)v3);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[31:16];
  uint32_t res32 = __SMLSDX (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t) (p1-p2+(int32_t)v3);
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
SMLALD / SMLALDX: Signed (eXchanged) multiply of 2x16bit data and int64_t accumulation, if overflow, return 2^64 modulo value
  uint64_t res64 = __SMLALD (uint32_t v1, uint32_t v2, uint64_t v3): res64 = (uint64_t)((p1+p2+(int64_t)v3) % (1<<64));
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[31:16];
  uint64_t res64 = __SMLALDX (uint32_t v1, uint32_t v2, uint64_t v3): res64 = (uint64_t)((p1+p2+(int64_t)v3) % (1<<64));
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
SMLSLD / SMLSLDX: Signed (eXchanged) multiply of 2x16bit data and int64_t accumulation product difference. if overflow, return 2^64 modulo value
  uint64_t res64 = __SMLSLD (uint32_t v1, uint32_t v2, uint64_t v3): res64 = (uint32_t)((p1-p2+(int64_t)v3) % (1<<64));
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[15:0] ); p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[31:16];
  uint64_t res64 = __SMLSLDX (uint32_t v1, uint32_t v2, uint64_t v3): res64 = (uint32_t)((p1-p2+(int64_t)v3) % (1<<64));
  p1 = (int32_t)((int16_t)v1[15:0]) * (int16_t)v2[31:16]; p2 = (int32_t)((int16_t)v1[31:16]) * (int16_t)v2[15:0]);
SMMLA: Sum the 3rd input with high 32-bit of the product of 2x32bit signed data. If overflow, return uint32_t casted
  uint32_t res32 = __SMMLA (uint32_t v1, uint32_t v2, uint32_t v3): res32 = (uint32_t)((p64>>32) + (int32_t)v3);
  p64 = (int32_t) v1 * (int32_t)v2;
CMSIS online document issues: All operation virtual codes miss sign-casting of the input data
Need programmer to prevent overflow

## Slide 17: Extract Bytes to extend/Accumulate (7) instructions – Function Tested OK
SXTB16 / UXTB16: low byte extraction and signed/unsigned extension to 16bit word, w/o input byte rotation
  SXTB16 / UXTB16 exTracts the low Byte of each 16-bit word and returns them as Signed/Unsigned-eXtended 16-bit words
    uint32_t res = __SXTB16(uint32_t v1): res[31:16] = (int16_t) ((int8_t)v1[23:16]); res[15:0] = (int16_t)((int8_t)v1[7:0]);
    uint32_t res = __UXTB16(uint32_t v1): res[31:16] = (uint8_t)v1[23:16]; res[15:0] = (uint8_t)v1[7:0];
  SXTB16_RORn performs SXTB16 with byte-rotated (right-shift rotate) input  missing definition in CMSIS-Core 2016
    uint32_t res = SXTB_RORn (uint32_t v1, immediate unit32_t rotate):
    res = SXTB16( rotate (v1,rotate) ); /* ‘rotate’ must be immediate value of rotate-bits in { 8, 16, 24 } */
SXTAB16 / UXTAB16: Sum the 1st input with extended low bytes of the 2nd input (as by SXTB/UXTB), returns accumulated words.
    uint32_t res = __SXTBA16(uint32_t v1, uint32_t v2): res[31:16] = (uint16_t)((int16_t)v1[31:16] + (int8_t)v2[23:16]); res[15:0] = (uint16_t)((int16_t)v1[15:0] + (int8_t)v2[7:0]);
    uint32_t res = __UXTBA16(uint32_t v1, uint32_t v2): res[31:16] = (uint16_t)(v1[31:16] + v2[23:16]); res[15:0] = (uint16_t)(v1[15:0] + v2[7:0]);
    If accumulation overflows, it just returns uint16_t casted value  Need programmer to prevent overflow by limiting the 1st input
USAD8 / USADA8: Sum 4 absolute byte-differences between two unsigned inputs, w/o the 3rd input
    uint32_t res = __USAD8(uint32_t v1, uint32_t v2): res = adiff1 + adiff2 + adiff3 + adiff4;
    adiff4 = abs(v1[31:24] – v2[31:24]); adiff3 = abs(v1[23:16] – v2[23:16]); adiff2 = abs(v1[15:8] – v2[15:8]); adiff1 = abs(v1[7:0] – v2[7:0]);
    uint32_t res = __USADA8(uint32_t, v1, uint32_t v2, uint32_t v3): res = v3 + adiff1 + adiff2 + adiff3 + adiff4;
    If USADA8 overflows, it just returns uint32_t casted value and ignores the carrier  Programmer can find carrier by the result and the 3rd input

## Slide 18: Saturated Signed ADD and Subtraction (8) instructions – Function Tested OK
QADD / QADD16 / QADD8, QSUB / QSUB16 / QSUB8 and QASX/QSAX, set xPSR/APSR.Q bit to ‘1’ if saturated  can check
  Summation/subtraction of 1x32-bit / 2x16bit / 4x8bit signed data, results saturated to [-231, 231-1] / [-215, 215-1] / [-27, 27-1], respectively
    uint32_t res = __QADD (uint32_t v1, uint32_t v2): res[31,0] = sat_i32 ((int32_t)v1 + (int32_t)v2);
    uint32_t res = __QADD16 (uint32_t v1, uint32_t v2): res[15:0] = sat_i16 ((int16_t)v1[15:0] + (int16_t)v2[15:0]); res[31:16] = sat_i16 ((int16_t)v1[31:16] + (int16_t)v2[31:16]);
    uint32_t res = __QADD8 (uint32_t v1, uint32_t v2): res[7:0] = sat_i8 ((int8_t)v1[7:0] + (int8_t)v2[7:0] ); res[15:8] = sat_i8 ((int8_t)v1[15:8] + (int8_t)v2[15:8]);
  res[23:16] = sat_i8 ((int8_t)v1[23:16] + (int8_t)v2[23:16] ); res[31:24] = sat_i8 ((int8_t)v1[31:24] + (int8_t)v2[31:24]);
    uint32_t res = __QSUB (uint32_t v1, uint32_t v2): res[31,0] = sat_i32 ((int32_t)v1 - (int32_t)v2 );
    uint32_t res = __QSUB16 (uint32_t v1, uint32_t v2): res[15:0] = sat_i16 ((int16_t)v1[15:0] - (int16_t)v2[15:0]); res[31:16] = sat_i16 ((int16_t)v1[31:16] - (int16_t)v2[31:16]);
    uint32_t res = __QSUB8 (uint32_t v1, uint32_t v2): res[7:0] = sat_i8 ((int8_t)v1[7:0] - (int8_t)v2[7:0]); res[15:8] = sat_i8 ((int8_t)v1[15:8] - (int8_t)v2[15:8]);
  res[23:16] = sat_i8 ((int8_t)v1[23:16] - (int8_t)v2[23:16]); res[31:24] = sat_i8 ((int8_t)v1[31:24] - (int8_t)v2[31:24]);
  High-Low-word-eXchanged summation and subtraction of 2x16bit signed data, results saturated to [-215, 215-1]
    uint32_t res = __QASX (uint32_t v1, uint32_t v2): res[31:16] = sat_i16 ((int16_t)v1[31:16] + (int16_t)v2[15:0]); res[15:0] = sat_i16 ((int16_t)v1[15:0] - (int16_t)v2[31:16]);
    uint32_t res = __QSAX (uint32_t v1, uint32_t v2): res[31:16] = sat_i16 ((int16_t)v1[31:16] - (int16_t)v2[15:0]); res[15:0] = sat_i16 ((int16_t)v1[15:0] + (int16_t)v2[31:16]);
CMSIS online document issues: Operation virtual code not as clear as above
  All operation virtual codes miss sign-casting of the input data
  QADD operation confusing: ‘res[31:0] = SAT(val1 + SAT(val2))’, the 2nd SAT should be removed

## Slide 19: Saturated UnSigned ADD and Subtraction (6) instructions – Function Tested OK
UQADD16 / UQADD8, UQSUB16 / UQSUB8 and UQASX / UQSAX, saturated to [0, 216-1] / [0, 28-1], but no touch on xPSR/APSR!!!
  Summation / Subtraction of 2x16bit / 4x8bit unsigned data
    uint32_t res = __UQADD16 (uint32_t v1, uint32_t v2):
    res[15:0] = sat_u16((uint16_t)v1[15:0] + (uint16_t)v2[15:0]); res[31:16] = sat_u16((uint16_t)v1[31:16] + (uint16_t)v2[31:16]);
    uint32_t res = __UQADD8 (uint32_t v1, uint32_t v2):
    res[7:0] = sat_u8 ((uint8_t)v1[7:0] + (uint8_t)v2[7:0] ); res[15:8] = sat_u8 ((uint8_t)v1[15:8] + (uint8_t)v2[15:8]);
  res[23:16] = sat_u8 ((uint8_t)v1[23:16] + (uint8_t)v2[23:16] ); res[31:24] = sat_u8 ((uint8_t)v1[31:24] + (uint8_t)v2[31:24]);
    uint32_t res = __UQSUB16 (uint32_t v1, uint32_t v2):
    res[15:0] = sat_u16 ((uint16_t)v1[15:0] - (uint16_t)v2[15:0]); res[31:16] = sat_u16 ((uint16_t)v1[31:16] - (uint16_t)v2[31:16]);
    uint32_t res = __UQSUB8 (uint32_t v1, uint32_t v2):
    res[7:0] = sat_u8 ((uint8_t)v1[7:0] - (uint8_t)v2[7:0]); res[15:8] = sat_u8 ((uint8_t)v1[15:8] - (uint8_t)v2[15:8]);
  res[23:16] = sat_u8 ((uint8_t)v1[23:16] - (uint8_t)v2[23:16]); res[31:24] = sat_u8 ((uint8_t)v1[31:24] - (uint8_t)v2[31:24]);
  High-Low-word-eXchanged summation and subtraction of 2x16bit unsigned data
    uint32_t res = __UQASX (uint32_t v1, uint32_t v2):
    res[31:16] = sat_u16((uint16_t)v1[31:16] + (uint16_t)v2[15:0]); res[15:0] = sat_u16((uint16_t)v1[15:0] -(uint16_t)v2[31:16]);
    uint32_t res = __UQSAX (uint32_t v1, uint32_t v2):
    res[31:16] = sat_u16((uint16_t)v1[31:16] - (uint16_t)v2[15:0]); res[15:0] = sat_u16((uint16_t)v1[15:0]+(uint16_t)v2[31:16]);
  !!!Note that programmer must be careful, as saturation is not detectable!!!

## Slide 20: Halved Signed ADD and Subtraction (6) instructions – Function Tested OK
SHADD16/SHADD8 & SHSUB16 / SHSUB8: ADD/SUB of 2x16bit / 4x8bit signed data, halved results in [-215, 215-1] / [-27, 27-1]
  uint32_t res = __SHADD16 (uint32_t v1, uint32_t v2):
  res[15:0] = ( (int16_t)v1[15:0] + (int16_t)v2[15:0] ) >> 1; res[31:16] = ( (int16_t)v1[31:16] + (int16_t)v2[31:16] ) >> 1;
  uint32_t res = __SHADD8 (uint32_t v1, uint32_t v2):
  res[7:0] = ( (int8_t)v1[7:0] + (int8_t)v2[7:0] ) >> 1; res[15:8] = ( (int8_t)v1[15:8] + (int8_t)v2[15:8] ) >> 1;
  res[23:16] = ( (int8_t)v1[23:16] + (int8_t)v2[23:16] ) >> 1; res[31:24] = ( (int8_t)v1[31:24] + (int8_t)v2[31:24] ) >> 1;
  uint32_t res = __SHSUB16 (uint32_t v1, uint32_t v2):
  res[15:0] = ( (int16_t)v1[15:0] - (int16_t)v2[15:0] ) >> 1; res[31:16] = ( (int16_t)v1[31:16] - (int16_t)v2[31:16] ) >> 1;
  uint32_t res = __SHSUB8 (uint32_t v1, uint32_t v2):
  res[7:0] = ( (int8_t)v1[7:0] - (int8_t)v2[7:0] ) >> 1; res[15:8] = ( (int8_t)v1[15:8] - (int8_t)v2[15:8] ) >> 1;
  res[23:16] = ( (int8_t)v1[23:16] - (int8_t)v2[23:16] ) >> 1; res[31:24] = ( (int8_t)v1[31:24] - (int8_t)v2[31:24] ) >> 1;
SHASX/SHSAX: High-low-word-eXchanged ADD & SUB of 2x16bit signed data, halved results in [-215, 215-1] / [-27, 27-1]
  uint32_t res = __SHASX (uint32_t v1, uint32_t v2):
  res[31:16] = ((int16_t)v1[31:16] + (int16_t)v2[15:0]) >>1; res[15:0] = ((int16_t)v1[15:0] - (int16_t)v2[31:16]) >>1;
  uint32_t res = __SHSAX (uint32_t v1, uint32_t v2):
  res[31:16] = ((int16_t)v1[31:16]) - (int16_t)v2[15:0]) >>1; res[15:0] = ((int16_t)v1[15:0] + (int16_t)v2[31:16]) >>1;
CMSIS online document issues: Operation virtual code wrong
  All operation virtual codes miss sign-casting of the input data
  All operation virtual codes miss ‘( )’ before shifting: eg. ‘res[15:0] = val1[15:0] + val2[15:0] >> 1’ is wrong
  !!! Note: -1>>1 = -1 !!! This must be concidered in DSP programming

## Slide 21: Halved UnSigned ADD and Subtraction (6) instructions – Function Tested OK
UHADD16 / UHADD8 and UHSUB16 / UHSUB8: ADD/SUB of 2x16bit / 4x8bit unsigned data, return halved results
  uint32_t res = __UHADD16 (uint32_t v1, uint32_t v2): sum16 in [0, 216-1]
  res[15:0] = (v1[15:0] + v2[15:0] ) >> 1; res[31:16] = (v1[31:16] + v2[31:16] ) >> 1;
  uint32_t res = __UHADD8 (uint32_t v1, uint32_t v2): sum8 in [0, 28-1]
  res[7:0] = (v1[7:0] + v2[7:0] ) >> 1; res[15:8] = (v1[15:8] + v2[15:8] ) >> 1;
  res[23:16] = (v1[23:16] + v2[23:16] ) >> 1; res[31:24] = (v1[31:24] + v2[31:24] ) >> 1;
  uint32_t res = __UHSUB16 (uint32_t v1, uint32_t v2): but diff16 in [-215, 215-1]
  res[15:0] = (v1[15:0] - v2[15:0] ) >> 1; res[31:16] = (v1[31:16] - v2[31:16] ) >> 1;
  uint32_t res = __UHSUB8 (uint32_t v1, uint32_t v2): diff8 in [-27, 27-1]
  res[7:0] = (v1[7:0] - v2[7:0] ) >> 1; res[15:8] = (v1[15:8] - v2[15:8] ) >> 1;
res[23:16] = (v1[23:16] - v2[23:16] ) >> 1; res[31:24] = (v1[31:24] - v2[31:24] ) >> 1;
UHASX / UHSAX: High-low-eXchanged ADD & SUB of 2x16bit unsigned data, halved results sum in [0, 216-1] but diff in [-215, 215-1]
  uint32_t res = __UHASX (uint32_t v1, uint32_t v2):
  res[31:16] = (v1[31:16] + v2[15:0]) >>1; res[15:0] = (uint16_t)(((int32_t)v1[15:0] - v2[31:16]) >>1);
  uint32_t res = __UHSAX (uint32_t v1, uint32_t v2):
  res[31:16] = (uint16_t)(((int32_t)v1[31:16]) - v2[15:0]) >>1); res[15:0] = (v1[15:0] + v2[31:16]) >>1;
CMSIS online document issues: Operation virtual code wrong
  All operation virtual codes miss sign-casting of the input data
  All operation virtual codes miss ‘( )’ before shifting: eg. ‘res[15:0] = val1[15:0] + val2[15:0] >> 1’ is wrong
  !!! Note: -1>>1 = -1 !!! thismust be concidered in DSP programming

## Slide 22: Full-resolution Signed ADD and Sub (6) instructions – Function Tested OK
SADD16 / SADD8 and SSUB16 / SSUB8: Full-resolution ADD/SUB of 2x16bit / 4x8bit signed data, with sign bit in xPSR/APSR.GE[3:0]
    uint32_t res =__SADD16 (uint32_t v1, uint32_t v2): sum32 = (int32_t)((int16_t)v1[15:0]) + (int16_t)v2[15:0]; res[15:0] = (uint16_t)sum32, GE[1:0] = (sum32>=0)? 3 : 0
    sum32 = (int32_t)((int16_t)v1[31:16] +(int16_t)v2[31:16]; res[31:16]=(uint16_t)sum32; GE[3:2] = (sum32>=0)? 3 : 0
    uint32_t res = __SADD8 (uint32_t v1, uint32_t v2): sum16 = (uint16_t)((int8_t)v1[7:0]) + (int8_t)v2[7:0]; res[7:0] =(uint8_t)sum16; GE[0] = (sum16>=0)? 1 : 0
    sum16 = (uint16_t)((int8_t)v1[15:8]) + (int8_t)v2[15:8]; res[15:8] =(uint8_t)sum16; GE[1] = (sum16>=0)? 1 : 0
    sum16 = (uint16_t)((int8_t)v1[23:16]) + (int8_t)v2[23:16]; res[23:16] =(uint8_t)sum16; GE[2] = (sum16>=0)? 1 : 0
    sum16 = (uint16_t)((int8_t)v1[31:24]) + (int8_t)v2[31:24]; res[31:24] =(uint8_t)sum16; GE[3] = (sum16>=0)? 1 : 0
    uint32_t res = __SSUB16 (uint32_t v1, uint32_t v2): diff32 = (int32_t)((int16_t)v1[15:0]) - (int16_t)v2[15:0]; res[15:0] = (uint16_t)diff32, GE[1:0] = (diff32>=0)? 3 : 0
    diff32 = (int32_t)((int16_t)v1[31:16]) - (int16_t)v2[31:16]; res[31:16]=(uint16_t)diff32; GE[3:2] = (diff32>=0)? 3 : 0
    uint32_t res = __SSUB8 (uint32_t v1, uint32_t v2): diff16 = (uint16_t)((int8_t)v1[7:0]) - (int8_t)v2[7:0]; res[7:0] =(uint8_t)diff16; GE[0] = (sum16>=0)? 1 : 0
    diff16 = (uint16_t)((int8_t)v1[15:8]) - (int8_t)v2[15:8]; res[15:8] =(uint8_t)diff16; GE[1] = (sum16>=0)? 1 : 0
    diff16 = (uint16_t)((int8_t)v1[23:16]) - (int8_t)v2[23:16]; res[23:16] =(uint8_t)diff16; GE[2] = (sum16>=0)? 1 : 0
    diff16 = (uint16_t)((int8_t)v1[31:24]) - (int8_t)v2[31:24]; res[31:24] =(uint8_t)diff16; GE[3] = (sum16>=0)? 1 : 0
SASX/SSAX: High-low-word-eXchanged full-resolution ADD & SUB of 2x16bit signed data, with sign bit in xPSR/APSR.GE[3:0]
    uint32_t res = __SASX (uint32_t v1, uint32_t v2): sum32 = (int32_t)((int16_t)v1[31:16]) + (int16_t)v2[15:0]; res[31:16] = (uint16_t)sum32, GE[3:2] = (sum32>=0)? 3 : 0
    diff32 = (int32_t)((int16_t)v1[15:0] - (int16_t)v2[31:16]; res[15:0] = (uint16_t)diff32; GE[1:0] = (diff32>=0)? 3 : 0
    uint32_t res = __SSAX (uint32_t v1, uint32_t v2): diff32 = (int32_t)((int16_t)v1[31:16]) - (int16_t)v2[15:0]; res[31:16] = (uint16_t)diff32, GE[3:2] = (diff32>=0)? 3 : 0
    sum32 = (int32_t)((int16_t)v1[15:0] + (int16_t)v2[31:16]; res[15:0] = (uint16_t)sum32; GE[1:0] = (sum32>=0)? 3 : 0
CMSIS online document issues: Operation virtual code not as clear as above
  All operation virtual codes miss sign-casting of the input data

## Slide 23: Full-resolution UnSigned ADD and Sub (6) instructions – Function Tested OK
UADD16 / UADD8 and USUB16 / USUB8: Full-resolution ADD/SUB of 2x16bit / 4x8bit unsigned data, with sign bit in xPSR/APSR.GE[3:0]
    uint32_t res =__UADD16 (uint32_t v1, uint32_t v2): sum32 = (int32_t)v1[15:0] + v2[15:0]; res[15:0] = (uint16_t)sum32, GE[1:0] = (sum32>=0)? 3 : 0
    sum32 = (int32_t)v1[31:16] +v2[31:16]; res[31:16]=(uint16_t)sum32; GE[3:2] = (sum32>=0)? 3 : 0
    uint32_t res = __UADD8 (uint32_t v1, uint32_t v2): sum16 = (int16_t) v1[7:0]) + v2[7:0]; res[7:0] =(uint8_t)sum16; GE[0] = (sum16>=0)? 1 : 0
    sum16 = (int16_t) v1[15:8]) + v2[15:8]; res[15:8] =(uint8_t)sum16; GE[1] = (sum16>=0)? 1 : 0
    sum16 = (int16_t) v1[23:16] + v2[23:16]; res[23:16] =(uint8_t)sum16; GE[2] = (sum16>=0)? 1 : 0
    sum16 = (int16_t) v1[31:24] + v2[31:24]; res[31:24] =(uint8_t)sum16; GE[3] = (sum16>=0)? 1 : 0
    uint32_t res = __USUB16 (uint32_t v1, uint32_t v2): diff32 = (int32_t) v1[15:0] - v2[15:0]; res[15:0] = (uint16_t)diff32, GE[1:0] = (diff32>=0)? 3 : 0
    diff32 = (int32_t) v1[31:16] - v2[31:16]; res[31:16]=(uint16_t)diff32; GE[3:2] = (diff32>=0)? 3 : 0
    uint32_t res = __USUB8 (uint32_t v1, uint32_t v2): diff16 = (int16_t) v1[7:0] - v2[7:0]; res[7:0] =(uint8_t)diff16; GE[0] = (sum16>=0)? 1 : 0
    diff16 = (int16_t) v1[15:8] - v2[15:8]; res[15:8] =(uint8_t)diff16; GE[1] = (sum16>=0)? 1 : 0
    diff16 = (int16_t) v1[23:16] - v2[23:16]; res[23:16] =(uint8_t)diff16; GE[2] = (sum16>=0)? 1 : 0
    diff16 = (int16_t) v1[31:24] - v2[31:24]; res[31:24] =(uint8_t)diff16; GE[3] = (sum16>=0)? 1 : 0
UASX/USAX: High-low-word-eXchanged full-resolution ADD & SUB of 2x16bit unsigned data, with sign bit in xPSR/APSR.GE[3:0]
    uint32_t res = __UASX (uint32_t v1, uint32_t v2): sum32 = (int32_t) v1[31:16]) + v2[15:0]; res[31:16] = (uint16_t)sum32, GE[3:2] = (sum32>=0)? 3 : 0
    diff32 = (int32_t) v1[15:0] - v2[31:16]; res[15:0] = (uint16_t)diff32; GE[1:0] = (diff32>=0)? 3 : 0
    uint32_t res = __USAX (uint32_t v1, uint32_t v2): diff32 = (int32_t) v1[31:16]) - v2[15:0]; res[31:16] = (uint16_t)diff32, GE[3:2] = (diff32>=0)? 3 : 0
    sum32 = (int32_t) v1[15:0] + v2[31:16]; res[15:0] = (uint16_t)sum32; GE[1:0] = (sum32>=0)? 3 : 0
CMSIS online document issues: Operation virtual code not as clear as above
  All operation virtual codes miss sign-casting of the input data

## Slide 24: To be tested Instructions

## Slide 25: CPU instructions and SIMD Multiplications
39 CPU instructions, especially for load and store.
Cycle count test
  Some intrinsic functions may contain input check, which is not always required but reduce speed, such as in __CLZ() and __PKHTB with ‘0’ check
Dual DPU slots and parallel process test
Optimize code
  Optimize most inner loop
  Best use of ‘register’ variables