## Slide 1: STRX M7 FPU & SIMD - Compiling ISSUEs and programing Advices
17th June 2021
Hong Li, Kai Gossner and Peter Kourzanov
hong.r.li@nxp.com

## Slide 2: STRX-RFE Cortex-M7 NEEDs SIMD & FPU programming
Improve STRX-RFE performance with embedded M7
  FW and API to control STRX-RFE HW
    Configure and control STRX-RFE modes with full RFE registers access
    Calibrate STRX-RFE on different working modes and chirp modes in runtime
  STRX-RFE chip test FW for Design for Test (DfT) support
    Test STRX in chip production testing
M7 DSP SIMD and FPU provides nice signal processing
  M7: 160MHz + 32kB RAM + 3.5MB (slower) shared memory
  FFT, DFT, SQRT, Log10/Log2, Atan/Angle…  rfeDsp math lib
  FPU: Single-precision floating-point accuracy arithmetic:
      HW instructions: SQRT, F2Q conversion, Mul+Add/Sub, etc.
  DPU: 32-bit arithmetic and fast 2x16bit and 4x8-bit SIMD
      e.g. Mul+Add/Sub instructions…

## Slide 3: M7 FPU & SIMD Compiling issues
Compiling and running issues listed in STRX-1986
  M3SA running hangs on elf image compiled by arm_clang
    Reason 1: Due to 64-bit Double instruction added by compiler  Solved
      Need compiling options for STRX-rfe M7: -mfloat-abi=hard; -mfpu=fpv5-sp-d16
      Arm_clang compiler needs also linker option: --fpu=FPv5-SP
    Reason 2: FPU is not enabled  Solved by calling enable FPU function
    Reason 3: Coding issue in m3saSimSupport code  Solved by Kai
    Reason 4: Give float varible to sim_printf()  Avoid printing float variable directly
      m3saSimSupport misses option %f in sim_printf(), but no plan to add due to limited effort
    Reason 5: Using a few 64-bit related SIMD intrinsic: SMLSLDX, SMLSLD, QASX  Avoid using them directly
      Need ARM support to dig into. So far can be bypassed if not use these 3 or 4 intrinsic
  M3SA running hangs on elf image compiled by arm_gcc  Avoid using arguments in main()
    Reason: when using main() arguments, arm_gcc 9 inserts 64-bit Double instruction
      Do not know why yet, but can easily bypass
  Linker reports error on missing ‘__aeabi_f2d’  Avoid below situations in coding
    Reason 1: Some float constant without ‘F’ or ‘f’ at the end of the number
    Reason 2: Give a float variable to sim_printf()

## Slide 4: ADVICEs on FPU and SIMD programming
Need to enable FPU
  #include “rfeDspMath.h” // get definitions, intrinsics and rfeDspMath functions
  main() {
  rfeDsp_enableFPU(); // Enable FPU
  …. }
Put ‘F’ or ‘f’ after each float constant in source to confirm single-precision floating point value: e.g float xF = 0.01F;
Print float variable by casting to interger when using M3SA sim_printf():
  e.g. sim_printf ( “Print float xF as %d e-6!”, ( int32_t ) ( xF * 1000000.0F ) );
Do not use SIMD intrinsic SMLSLDX, SMLSLD, QASX, or update SIMD status register e.g. APSR.Q
Do not do shift by 32 bit especially on a negative value
  e.g. int32_t k32 = -100; k32 >> 32 can be wrong. (also Note k32 >> 16 is -1, due to appended sign bit)
Recommend to use standard C arithmetic operands in floating process, instead of FPU instructions unless you do know them
  Compiler performance is quite OK (many our own FPU intrinsic are not tested yet)
Recommend to use type casting to do integer-float conversion
Do not use FPU status register e.g. clean FPSCR exception flags
  Need ARM support to check our code
  __STATIC_INLINE void rfeDsp_enableFPU ( void ) /* Enable FPU */
  {
  *( ( volatile uint32_t* )0xE000ED88 ) |= 0xful << 20ul ;
  __DSB(); // _dsb();
  __ISB(); // _isb();
  }

## Slide 5: IEEE754 single-precision floating-point value definition
One float number takes 32bits in the following format
  b31: sign bit, 1  Negative; 0  Positive
  b30-b23: 8-bit signed Exponent with bias 127, i.e. b30-b23 = Expo + 127
  b22-b0: 23-bit mantissa or fractional bits
  Value is: (-1)b31 * 2 ^((b30b29…b23)2-127) * (1.b22b21…b1b0 )2
Special definition and exceptions
Expo b30-b23 | Fraction b22-b0 == 0 | Fraction b22-b0 != 0 | Fraction b22-b0 != 0 | Equation
0 | zero | Small values | Small values | (-1)b31 * 2-126 * (0.fraction)2
[0,0xFE] | Normal values |  |  | (-1)b31 * 2 Expo-127 * (0.fraction)2
0xFF | +- Infinity | NaN |  | 

## Slide 6: Current results
Compiler issues solved for using SIMD and using FPU instructions
70% M7 DSP math library implementation completed
  Float-Q31/15.n conversion, SQRT & complex ABS, polynomial, min/max/mean/std, sorting, One-bin / dual-bin real input DFT
  IMD and FPU real input FFT: FPU FFT is about 1.5x slower than SIMD FFT ( FPU FFT maybe more optimized )
    Shared memory FFT is ~2x slower
  In progress (Marinus)
    Log2 & log 10
    Arctan / Angle
  To be implemented:
    Single-bit input FFT: just need bit-int16_t conversion + SIMD FFT
    Complex input FFT and Histogram
  Further math function speed optimization only if really required by DfT or calibration teams
M7 programming issues
  Intrinsic definition for using FPU mul+add/sub…
  Intrinsic definition for 4 advanced SIMD instructions
  Program State register usage and reset, e.g. APSR.Q reset, FPU FPSCR usage for divided by zero, conversion saturation, etc.
Armclang FFT size | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384
SIMD FFT cycles | 260 | 481 | 951 | 1870 | 3845 | 8035 | 16396 | 36173 |  |  |  | 
on shared-mem |  |  |  |  |  |  |  | 64124 | 138538 | 298013 | 639766 | 1362057
FPU FFT cycles | 386 | 713 | 1293 | 2557 | 5359 | 11473 | 24377 | 55226 |  |  |  | 
on shared-mem |  |  |  |  |  |  |  | 96797 | 212755 | 462717 | 998549 | 2139391