## Slide 1: Rfe-IRQ
January 2023
Pedro Ferrão

## Slide 2: RFE-IRQs
Motivation:
Allow rfem7 to generate IRQs to the appM7, a53 cores for:
  Non-blocking rfeDriver APIs;
  State change notifications;
  Other notifications;

## Slide 3: RFE-IRQs
How inter-processor communication (IPC) is handled:
IPC is handled via Miscellaneous System Control Module (MSCM)
Each core supports 4 IPC interrupts:
  Per STRX-7389, IPC_IRQ_1 was agreed
On the sending core: An interrupted is generated by writing to a specific register (GR).
On the receiving core: An interrupt must be acknowledged by writing to a specific register (SR).
 | M7 core | a53 core
IPC_IRQ_0 | 1 | 33
IPC_IRQ_1 | 2 | 34
IPC_IRQ_2 | 3 | 35
IPC_IRQ_3 | 4 | 36

## Slide 4: RFE-IRQs
Generating an interrupt (1/2):
An interrupt is generated by writing 1 to the following register IRCPnIGRm, where:
  n: Is the target core:
  m: Is the IPC interrupt number
rfeM7 can trigger an IPC_IRQ_1 interrupt on:
  appM7 core by writing 1 to IRCP0IGR1
  a53 core by writing 1 to IRCP2IGR1
appM7 core | 0
rfeM7 core | 1
a53 core | 2
BBS DSP core | 3

## Slide 5: RFE-IRQs
Generating an interrupt (2/2):
Writing to IRCPnIGRm will change a bit (1 << x) on the respective IRCPnISRm register, where:
  x: Corresponds to the source core (platform cores):
The respective core will be interrupted (provided that, it was interrupts properly routed and enabled).
  To acknowledge the interrupted IRCPnISRm bit needs to be cleared.
  This bit can also be clear by the initiating core, or any core configured as trusted.
m7 cores | 0
a53 core | 2

## Slide 6: RFE-IRQs
Changes on PR1192 (rfem7 side):
MSCM register map (offsets and fields from documentation)
MSCM driver with the following APIs:
  void rfeHwMscm_init( RFE_ERROR_FUNCTION_PARAMETER )
  Initializes MSCM driver, for now it just clears any IPC_IRQ_1 pending on a53/appM7, the remaining
  actions for this API will need to be agreed upon.
  void rfeHwMscm_raiseIrq( rfeHwMscm_target_t target, RFE_ERROR_FUNCTION_PARAMETER )
Raises an IRQ (IPC_IRQ_1) on the target:
    rfeHwMscm_target_appM7_e,
    rfeHwMscm_target_a53_e,
    rfeHwMscm_target_all_e

## Slide 7: RFE-IRQs
Changes on PR1192 (rfem7 side):
MSCM driver API unit tests:
  Raise an interrupt with the driver API
  Verify that the interrupt pending bit is set
  Unfortunately, there is currently no way to automate a CI test, to actually test the interrupt on appM7/a53 side…
Small test application rfeIrqTest:
  This application will trigger an alternating interrupt to appM7/a53 every second (each core should receive an interrupt from rfem7 every two seconds (plus some clock jitter)).

## Slide 8: RFE-IRQs
Changes on PR1192 (rfeDriver/apps side):
Example application for appM7/a53, rfeAppInterruptExample:
  This application will setup the proper interrupt handler (NVIC on m7, GIC on a53), and go into a lower-power mode (WFI – wait for interrupt)
  When executed together with rfeIrqTest, it will output ‘Interrupted!’ every two seconds and go back into lower-power mode