## Slide 1: SW WDT Config
October 2022

## Slide 2: motivation
Need to trigger a FuSa error if the M7 is stuck during operation
Use the SW WDT from the rfe M7 for this
Refresh the timer periodically, based on if a radarCycle is running or not

## Slide 3: Sw wdt in the fsm
Two timeouts are needed for the SW WDT – one for rfe_configure and one for the radar cycle FSM
See slide 5 for more details.

## Slide 4: Proposal for sw WDT
RFE running in the main FSM loop
  Refresh time = Radar Cycle Duration (to avoid reconfiguration during radar cycles)
  Timeout = 1.25* radar cycle duration (125%, needs to be verified)
  Since a command can come at any point during the main FSM, the timeout should account for the maximum delay possible in handling commands (other than rfe_configure)
Rfe_configure
  Refresh the WDT
  Reconfigure WDT with timeout = 200ms -> Is 200ms enough for rfe_configure? Is more time needed?
End of rfe_configure
  Refresh the WDT
  Reconfigure WDT with timeout = radar cycle duration
Radar Cycles
  Re-configure -> update config can reconfigure the radar cycle duration -> reconfigure in such a case
  Refresh the beginning of radar cycles
  No need for reconfiguration for normal operations
Needs to be tested for various profiles

## Slide 5
RFE SW Watchdog Configuration and refresh in the MainFSM
State/command | SW Watchdog behavior
RFE Init (FuSaManager Init_ | Configure WDT to 40ms Refresh every 20 ms
Beginning of rfe_configure() | Refresh WDT Enable WDT with timeout = 200ms (depends on the configuration time)
End of rfe_configure() | Refresh WDT Enable WDT with timeout = Radar Cycle Duration + overhead
Configured state | No Change in WDT config Timeout = Radar Cycle Duration + overhead Refresh every radar cycle duration
Radar Cycle Start | No Change in WDT Config Refresh WDT
Radar Cycle End | No change in WDT Config WDT goes back to configured
Radar Cycle Idle | For synchronizing, refresh every 10 ms so that WDT does not expire on rfeSwMainFsm_setNextRadarCycleStartTime. Update only when rfeSwMainFsm_setNextRadarCycleStartTime is called
Bad Config (back to initialized) | No change in WDT config Refresh WDT every radar cycle duration
Radar Cycle updateConfig | Refresh and re-configure radar cycle if updateConfig is called. Enable WDT with timeout = New radar cycle duration + overhead

## Slide 6: Sw watchdog interface
Configuration available with the following settings:
  Timeout in ticks for the watchdog
  Service mode to refresh the WDT: fixed sequence, keyed sequence
  Clock source: Oscillator clock/system clock
API to refresh the WDT
API to enable/disable the WDT
Internal API to reset the WDT (if WDT error is triggered, there is an internal API to disable the WDT for FIT 2)
More details in the following slides

## Slide 7: Sw watchdog interface
**
* \brief This function configures the SW Watchdog timer
*
* \details This function configures the SW Watchdog timer. Called by rfeSwFuSaMngr_init
*
* \pre NIL
*
* \param [in] clockSource Clock source for the watchdog timer
*
* \param [in] timeout Timeout in ticks
*
* \param [in] mode Service mode
*
* \param [in,out] RFE_ERROR_FUNCTION_PARAMETER - Error handling parameter:
* On success rfeError_error_none_e is returned
*
* \return NIL
*
* \post NIL
*
* \ingroup NIL
*/
void rfeHwSwt_configureSwWdt(
rfeHwSwt_clockSelect_t clockSource,
uint32_t timeOut,
rfeHwSwt_serviceMode_t mode,
RFE_ERROR_FUNCTION_PARAMETER
);

## Slide 8: Sw watchdog interface
/**
* \brief This function refreshes the SW Watchdog timer
*
* \details This function refreshes the SW Watchdog timer. Called by rfeSwMainFsm periodically
*
* \pre NIL
*
* \param [in] mode service mode
*
* \param [in,out] RFE_ERROR_FUNCTION_PARAMETER - Error handling parameter:
* On success rfeError_error_none_e is returned
*
* \return NIL
*
* \post NIL
*
* \ingroup NIL
*/
void rfeHwSwt_refreshSwWdt(
rfeHwSwt_serviceMode_t mode,
RFE_ERROR_FUNCTION_PARAMETER
);

## Slide 9: Sw watchdog interface
/**
* \brief This function enables the SW Watchdog timer
*
* \details This function enables the SW Watchdog timer. Called by rfeSwMainFsm periodically
*
* \pre NIL
*
* \param [in] enable - enable/disable the watchdog
*
* \param [in,out] RFE_ERROR_FUNCTION_PARAMETER - Error handling parameter:
* On success rfeError_error_none_e is returned
*
* \return NIL
*
* \post NIL
*
* \ingroup NIL
*/
void rfeHwSwt_enableSwWdt(
rfeHwSwt_watchdogEnable_t enable,
RFE_ERROR_FUNCTION_PARAMETER
);

## Slide 10: Sw watchdog interface
/**
* \brief This function resets the SW Watchdog timer
*
* \details This function resets the SW Watchdog timer. Called by rfeSwFit2
*
* \pre NIL
*
* \param [in,out] RFE_ERROR_FUNCTION_PARAMETER - Error handling parameter:
* On success rfeError_error_none_e is returned
*
* \return NIL
*
* \post NIL
*
* \ingroup NIL
*/
void rfeHwSwt_resetSwWdt(
RFE_ERROR_FUNCTION_PARAMETER
);