## Slide 1: Tx BIST design
2022

## Slide 2: Txs+Txbist structure
x2
7-bit Phase-rotator
IQ
DAC
Dig-Controller
PPD
VGA
To ATB ADC
x2
7-bit Phase-rotator
IQ
DAC
Dig-Controller
From LOI
From LOI
Measured TX
Reference TX
ATB ADC Capture
PPD
ATB ADC Capture

## Slide 3: Block diagrams

## Slide 4: Block Diagram: Txbist main operation
PA
Coupler
TX1 phase φ1 : to be measured.
TX2 phase φ2 : 0º → 360º
Vout = A1.cos(Δφ)
PA
TXBIST
Measured TX
Reference TX
TXbist main operation : measure the TX phase shift
Vout_txbist = A2.cos(Δφ)
fft(Vout_txbist), N pts
Phase TX1
Coupler
VGA

## Slide 5: TX BIST Phase difference

## Slide 6
Eol done at a Freq (programmable)
TX1/2 PR INL/DNL to be calibrated
EoL done at the reference power for Tx1/2
7dBm +/-1dB
  ( 7dBm because Low output power with stable gain across temperature)
VGA gain chosen to code 4 to have the right amplification
corresponding to the chosen power regarding the LUT (see next slide)
End of line measurement to be done and stored
TXbist main operation : measure tx to TX phase difference
VGA
To ATB ADC
TX1 : Fixed phase
Reference TX
ATB ADC Capture
φ2 : 0º → 360º
(Config 1 : 45° x 8 steps)
Load BIST profile
VGA gain to code 4
φ1 : 0º
Fusa TxBIST measurement
VGA
To ATB ADC
TX1 : Fixed phase
Reference TX
ATB ADC Capture
+FFT
φ2 : 0º → 360º (45° steps/8steps)
φ1 : 0º
+10°
-10°
Config 1 : 45° x 8 steps
Load TX1 and Tx2 profiles for TxBIST measurement
fft
fft
Threshold programmable
(Based on validation)
NB: TXBIST is only working with 2 consecutive Tx channels enabled

## Slide 7: TX BIST Phase STEPS

## Slide 8
TXbist main operation : measure tx to TX phase STEP
VGA
To ATB ADC
Reference Tx : Fixed phase
Measured TX
ATB ADC Capture
: 0º → 360º (45° /8steps)
φ1 : 0º
Hilbert transform
(FFT+IFFT)
Analytic signal (complex)
Real signal
Atan
8 phases: … - 45°
8 complex samples
8 real samples
Reference Tx
Measured Tx
+10°
-10°
TX profile for BIST is loaded, same configuration as for phase difference
Programmable threshold
Threshold to be determined regarding validation data
Fault injection models need to be done to validate this new method
NB: This new method is chosen to be the plan of record to reduce the emission time
Decisions taken during safety meetings:
Threshold programmable
(Based on validation)

## Slide 9: Design FLOW

## Slide 10: Design flow diagram (rfeSwBist_calculateTxBistParameters)
IF signal phase calculation
Txs On, TxBist On
rfeSwBist_calculateFftOfIfSignal(
Set reference Tx phase
Measure IF signal sample
Set Measured Tx phase
TxBIST Calibration
IF signal samples measurement
FFT processing
Hilbert transform
rfeSwBist_measureTxBistIfSignalSamples
Get Power
Set VGA gain
rfeSwBist_calculateMaximumPhaseStepDeviation
rfeSwBist_calibrateTxBist
IF signal FFT calculation
Phase step deviation calculation
rfeSwBist_calculateIfSignalPhase
Arctan

## Slide 11: TX BIST
/**
* rfeSwBist_txBistParam_t type defines the parameters and results in TxBist.
*/
typedef struct {
/** Measured calibrated power at Txs */
float targetPower;
/** Used frequency for Bist */
uint32_t txFrequencyForBist;
/** Enabled Txs */
uint8_t selectedTxs;
/** Input phasesdiff thresholds at txbists */
float phaseDiffThreshold;
/** Input phasesStep thresholds at txs */
float phaseStepThreshold;
/** Measured phases at txbists */
float phaseMeas[RFE_TXBIST_COUNT];
/** Measured zero Hour phases at txbists */
float zeroHourPhaseMeas[RFE_TXBIST_COUNT];
/** Phase difference deviation from zero hour measurement at txbists */
float phaseDiffDeviation[RFE_TXBIST_COUNT];
/** Maximum measured phase step deviation from setted phase step at txbists */
float maximumPhaseStepDeviation[RFE_TX_COUNT];
} rfeSwBist_txBistParam_t;

## Slide 12: TX BIST
Function that will be used to enable TxBist
rfeHwTx_subcomponentEnabling( txToUse,
currentSubcomponent,
enableSubcomponent,
RFE_ERROR_FUNCTION_ARGUMENT );
Enum structure that enumerates the 3 txbists
typedef enum
{
rfeSwBist_ txbistIndex _1_e,
rfeSwBist_ txbistIndex _2_e,
rfeSwBist_ txbistIndex _2_e
} rfeSwBist_txbistIndex_t;

## Slide 13: Txbist Calibration

## Slide 14: TxBIST Calibration function
void rfeSwBist_calibrateTxBist(
const rfeSwBist_txBistParam_t *pTxBistParam,
rfeSwBist_txBistIndex_t txBistInd,
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 15: Txbist calibration : specification
The aim of the calibration is to provide a signal whose amplitude Vout is in the dynamic range of the ADC. Additionally, system studies has shown that too low level would lead to a degradation of the phase accuracy. Consequently, the output differential level should be between 0.2Vpp and 1.2Vpp.
The calibration is made with VGA_gain using a simple LUT.
PA
VGA
Coupler
TX1 phase φ1
TX2 phase φ2 : 0º → 360º
Vout = A1.cos(Δφ)
PA
TXBIST
TX1
TX2
Vout_final = Vout.cos(Δφ)
VGA_gain
ADC

## Slide 16: Txbist calibration (set vga gain)
Structure that enumerates the txbist VGA gains
typedef enum
{
rfeHwTx_txBistVGACtrl_0dB_e = 0x01u, /**< rfeHwTx_txBistVGACtrl_0dB_e, default value for TX BIST VGA Calibration */
rfeHwTx_txBistVGACtrl_5dB_e = 0x02u, /**< rfeHwTx_txBistVGACtrl_5dB_e */
rfeHwTx_txBistVGACtrl_10dB_e = 0x04u,/**< rfeHwTx_txBistVGACtrl_10dB_e */
rfeHwTx_txBistVGACtrl_15dB_e = 0x08u,/**< rfeHwTx_txBistVGACtrl_15dB_e */
rfeHwTx_txBistVGACtrl_20dB_e = 0x10u,/**< rfeHwTx_txBistVGACtrl_20dB_e */
rfeHwTx_txBistVGACtrl_25dB_e = 0x20u /**< rfeHwTx_txBistVGACtrl_25dB_e */
} rfeHwTx_txBistVGACtrl_t;
Function to set the VGA gain of txbist
void rfeHwTx_bistCtrlVGASetter(
rfe_txIndex_t txSelected,
rfeHwTx_txBistVGACtrl_t vgaCtrlGain,
RFE_ERROR_FUNCTION_PARAMETER
);

## Slide 17: IF SIGNAL measurement

## Slide 18: IF signal measurement function
Function that will measure the IF signal sample
void rfeSwBist_measureTxBistIfSignalSamples(
rfeHwAtb_atbMaster_t selectedAtbX,
float IfSignalMeas[RFE_SAMPLES_COUNT],
rfeSwBist_txBistIndex_t txBistInd,
rfe_txIndex_t txToMeasure,
rfe_txIndex_t txRef,
rfe_phaseRotation_t txToMeasurePhase,
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 19: IF signal samples measurements
Example of 8 IF samples measurement for one period

## Slide 20: IF signal samples measurement
Number of phases in one period: 8
Number of periods:1/ 2
Set reference Tx phase
Measure IF signal sample
Set Measured Tx phase
Function to set the PR phase
void rfeHwTx_overridePrPhaseSetter(
rfe_txIndex_t txSelected,
bool overRidePrPhase,
rfe_phaseRotation_t prPhase,
RFE_ERROR_FUNCTION_PARAMETER );
Function that will measure the actual IF signal sample
void rfeSwBist_measureTxBistIfSignalSamples(
rfeHwAtb_atbMaster_t selectedAtbX,
float IfSignalMeas[RFE_SAMPLES_COUNT],
rfeSwBist_txBistIndex_t txBistInd,
rfe_txIndex_t txToMeasure,
rfe_txIndex_t txRef,
rfe_phaseRotation_t txToMeasurePhase,
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 21: IF signal FFT calculation

## Slide 22: FFT calculation function
Function that will calculate the FFT of the measured IF signal
void rfeSwBist_calculateFftOfIfSignal(
float IfSignalMeas[RFE_SAMPLES_COUNT],
cfloat32_t fftResult[RFE_SAMPLES_COUNT / 2],
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 23: PHASE calculation

## Slide 24: Phase calculation function
Function that will calculate the phase of the IF signal from calculated FFT of the measured IF signal
float rfeSwBist_calculateIfSignalPhase(
cfloat32_t fftResult[RFE_SAMPLES_COUNT / 2],
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 25: Phase Calculation

## Slide 26: PHASE STEP calculation

## Slide 27: Phase calculation function
Function that will calculate the phase step from calculated FFT of the measured IF signal
float rfeSwBist_calculateMaximumPhaseStepDeviation(
cfloat32_t fftResult[RFE_SAMPLES_COUNT / 2],
RFE_ERROR_FUNCTION_PARAMETER)

## Slide 28: TXBIST REquirements