## Slide 1: RfeswocOTP in SAF85xx

## Slide 2: OTP Programming
Previous Design: There are three register <>_trim_get, <>_trim_set,
<>_trim, where
- <>_trim is calling the <>_trim_set API.
- <>_trim_set is used to read OTP value from shadow register using
<>_trim_get API and write it into HW Ip register using rfeHwSpi_modify API
- <>_trim_get API is used to read OTP value from shadow register.
These 3 API has been implemented for every OTP value and called from rfeSwOcOtp_<subsystem>_trim API to write OTP value into HW Ip.
Updated Design:
-- Two table will be kept with the default OTP values and OTP values after reading shadow register.
-- A static table will be kept with the details of OTP source(shadow register) and destination(HW IP) register details.
-- rfeSwOcOtp_readOTPFuse – This API will read OTP valid bits and OTP trim bits from shadow register and populate local table
-- rfeSWOcOtp_DistributeOtp –This API will take OTP trimValidIdentifier, array of default OTP table startIndex and endIndex as input. It will parse through the static table using Valid trim identifier and get the source and destination register details from the static table for the Valid trim identifier and compute src valid register address, start offset using trimValidIdentifier.
OTP source register value will be retrieved (using rfeSwOcOtp_trim_get API) and be written into HW IP(using rfeHwSpi_modify API) for all the register requested using startIndex and endIndex.
-- Submodules can keep a table having the details of trimValidIdentifier, startIndex and endIndex and call rfeSWOcOtp_DistributeOtp API in a loop for every item in the table to write OTP value.

## Slide 3
HW IP Register
OcOtp
OTP Fuse
Shadow Registers
OcOtp Sw Unit
rfeSwOcOtp_defaults
(Default OTP Table)
rfeSwOcOtp_otpValue
(OTP Table created from OTP Fuse )
rfeSwOcOtp_trimValid
(OTP Trim Valid Table created from OTP Fuse)
spiBasedRegTable & hwBasedRegTable
(Table having details of Source and Destination reg details

## Slide 4
RFESwInit
rfeSwOcOtp_readOTPFuse
RFESwOcOtp
rfeSwOcOtp_<Modules*>_trim
rfeSWOcOtp_DistributeOtp
Notes: Modules are ATB, Chirppll, Gldo, Ldo_Dig, Ldo_Pdc, Lo_interface, Mcgen, Rx_Bist, Tsense, Tx etc

## Slide 5: API
void __attribute__((noinline)) rfeSwOcOtp_readOTPFuse( RFE_ERROR_FUNCTION_PARAMETER )
-This API will be used to call OTP valid and OTP trim bits from shadow register and populate into local table
void rfeSWOcOtp_DistributeOtp(rfeSwOcOtp_otpTrimValidIdentifier_t trimValidIdentifier, uint8_t startIdx, uint8_t endIdx, RFE_ERROR_FUNCTION_PARAMETER);
- This API will be used to read OTP value from shadow register using rfeSwOcOtp _trim_get and write into HW IP.
uint32_t __attribute__((noinline)) rfeSwOcOtp_trim_get(rfeSwOcOtp_otpTrimValidIdentifier_t otpTrimValidIdentifier, uint8_t arrayOffset, uint8_t dataStartBit, uint8_t dataNumOfBits, RFE_ERROR_FUNCTION_PARAMETER)
- This API will be used to get OTP value. First it will check the valid trim bits, if its valid it will return the value from OTP table which was created after reading shadow register, otherwise it will read from default table.
void rfeSwOcOtp_<Modules>_trim( uint32_t array[39], RFE_ERROR_FUNCTION_PARAMETER )
- Main API to write trims for individual Ip, which will make use of rfeSWOcOtp_DistributeOtp API to distribute OTP.

## Slide 6: Data structure
typedef struct
{
/** Destination module SPI address */
rfeHwSpi_module_t DstMod;
/** No of Otp bits */
uint8_t NoOfOtpBit;
/** Destination register address */
rfeHwReg_offset_t DstReg;
/** Bit field start position in destination register */
uint8_t DstPos;
/** the SrcAddr is the relative address in the default OTP table (starting from 0, step of 4) */
uint8_t SrcAddr_TableOffset;
/** Bit field start position in source table */
uint8_t SrcPos;
} rfeSwOcOtp_otpSpiBasedRegDescriptor_t;
typedef struct
{
/** Destination module SPI address */
rfeHwReg_base_t DstMod;
/** No of Otp bits */
uint8_t NoOfOtpBit;
/** Destination register address */
rfeHwReg_offset_t DstReg;
/** Bit field start position in destination register */
uint8_t DstPos;
/** the SrcAddr is the relative address in the default OTP table (starting from 0, step of 4) */
uint8_t SrcAddr_TableOffset;
/** Bit field start position in source table */
uint8_t SrcPos;
} rfeSwOcOtp_otpHwBasedRegDescriptor_t;

## Slide 7: Data structure
//Enum for every valid trim identifier
typedef enum
{
rfeSwOcOtp_otpTrimValidList_GldoBgGldo1v45_e = 0,
rfeSwOcOtp_otpTrimValidList_GldoOvuvGldo1v45_e = 1,
rfeSwOcOtp_otpTrimValidList_Lox4TuneFreq_e = 2,
………….
………….
rfeSwOcOtp_otpTrimValidList_ChirpGenCp_e = 48,
rfeSwOcOtp_otpTrimValidList_ChirpGenRcosc_e = 49
} rfeSwOcOtp_otpTrimValidIdentifier_t;
//Structure for Subsystem level OTP distribution
typedef struct
{
// Trim valid identifier
rfeSwOcOtp_otpTrimValidIdentifier_t trimValidIdentifier;
// Start index of the OTP register for the trimValidIdentifier
uint8_t startIdx;
// End index of the OTP register for the trimValidIdentifier
uint8_t endIdx;
} rfeSwOcOtp_otpTable_t;

## Slide 8: Sample API Implementation(ATB)
void rfeSwOcOtp_Atb_trim( uint32_t array[39], RFE_ERROR_FUNCTION_PARAMETER )
{
rfeSwOcOtp_otpTable_t rfeSwOcOtp_atb_Trim_Table[] = {/* trimValidIdentifier, startIdx, endIdx */
{rfeSwOcOtp_otpTrimValidList_AtbBg_e, 0, 0},
{rfeSwOcOtp_otpTrimValidList_AtbRcal_e, 0, 3},
{rfeSwOcOtp_otpTrimValidList_AtbAdcHwCtrl_e, 0, 5} };
for(i = 0; i < rfeSwOcOtp_atb_Trim_count; i++)
{
rfeSWOcOtp_DistributeOtp(rfeSwOcOtp_atb_Trim_Table[i]. trimValidIdentifier, array, rfeSwOcOtp_atb_Trim_Table[i].startIdx, rfeSwOcOtp_atb_Trim_Table[i].endIdx);
}
}

## Slide 9: OcOtp unit Test approach
Hw Register
Rfe OcOTP SW Unit
OcOTP SW UnitTest
Check if the RfeSwInit trims correctly
Call other functions that were not called from RfeSwInit
Test SW trims
Rfe SwInit
OTP shadow register
Default Table

## Slide 10: Python script to convert OTP trimming strategy to distribute array
Python modules used: xlrd
Input : OTP trimming strategy ( Ex. STRX_RFE_SOC_Trimming_strategy_TO1_v46.xlsm)
Output: text file with distribute table
In the script, parsing through the excel,
  Parsing through the sheet “TRIM VALID” and get the data of Trim valid item.
  Parse though the column Trim flow item /Trim valid item, and for each value of Trim flow/Trim valid
  Item, get the OTP register details. Get Destination IP module, bus, IP register, bit field and create macros for these, and get OTP fuse register details(src addr, start bit, no of bit and pointer to default OTP table).
  Update all these details in a table format as described below.
  static const rfeSwOcOtp_otpTableDescriptor_t rfeSwOcOtp_otpDistributeTable[OTP_TRIM_REG_COUNT] = {
  {RFE_HW_GLDO_BG_TRIM_SETDC_BG_GLD1V45_MSK, RFE_HW_GLDO_BG_TRIM_REG, RFE_HW_GLDO_BG_TRIM_SETDC_BG_GLD1V45_SHF, RFE_HW_SPI_GLDO_MODULE, _2B0, 0x2B0, 28, 4},
  .....
  };
  Note: These macros are defined in header file in rfe SW code repo.

## Slide 11
Old OTP defaults
uint32_t rfeSwOcOtp_defaults[] = {
[rfeSwOcOtp_otpRegAddr_284_e] = 0xa4b3b80b, // BITS_MASK(TEMP_2,0xa4b3,16,16)|BITS_MASK(TEMP_2,0xb80b,0,16)|BITS_MASK(TEMP_3,0xa4b3,16,16)|BITS_MASK(TEMP_3,0xb80b,0,16)|BITS_MASK(TEMP_4,0xa4b3,16,16)|BITS_MASK(TEMP_4,0xb80b,0,16)|BITS_MASK(TEMP_1,0xa4b3,16,16)|BITS_MASK(TEMP_1,0xb80b,0,16)
[rfeSwOcOtp_otpRegAddr_288_e] = 0x7574, // BITS_MASK(TEMP_2,0x7574,0,16)|BITS_MASK(TEMP_3,0x7574,0,16)|BITS_MASK(TEMP_4,0x7574,0,16)|BITS_MASK(TEMP_1,0x7574,0,16)
[rfeSwOcOtp_otpRegAddr_28C_e] = 0x0, // BITS_MASK(TEMP_2,0x0,16,16)|BITS_MASK(TEMP_3,0x0,0,16)
[rfeSwOcOtp_otpRegAddr_290_e] = 0x0, // BITS_MASK(TEMP_4,0x0,16,16)|BITS_MASK(TEMP_1,0x0,0,16)
[rfeSwOcOtp_otpRegAddr_294_e] = 0x121f5, // BITS_MASK(LDO_PDC,0x15,0,5)|BITS_MASK(LDO_DIG,0x9,13,4)|BITS_MASK(LDO_DIG,0x0,9,4)|BITS_MASK(LDO_DIG,0xf,5,4)
[rfeSwOcOtp_otpRegAddr_2A4_e] = 0x42, // BITS_MASK(RX,0x8,3,4)|BITS_MASK(RX,0x1,1,2)
[rfeSwOcOtp_otpRegAddr_2B0_e] = 0x80f80080, // BITS_MASK(GLDO,0x8,28,4)|BITS_MASK(GLDO,0x0,24,4)|BITS_MASK(GLDO,0xf,20,4)|BITS_MASK(GLDO,0x8,16,4)|BITS_MASK(GLDO,0x0,12,4)|BITS_MASK(GLDO,0x8,4,4)|BITS_MASK(GLDO,0x0,0,4)
[rfeSwOcOtp_otpRegAddr_2B4_e] = 0x1f21e, // BITS_MASK(GLDO,0xf,13,4)|BITS_MASK(GLDO,0x9,9,4)|BITS_MASK(GLDO,0x0,5,4)|BITS_MASK(GLDO,0xf,1,4)
[rfeSwOcOtp_otpRegAddr_2B8_e] = 0x13, // BITS_MASK(MCGEN,0x13,0,5)
[rfeSwOcOtp_otpRegAddr_2BC_e] = 0x2, // BITS_MASK(LO_INTERFACE,0x2,0,2)
[rfeSwOcOtp_otpRegAddr_2C0_e] = 0x210840, // BITS_MASK(TX_1,0x8,13,5)|BITS_MASK(TX_2,0x8,8,5)|BITS_MASK(TX_3,0x8,3,5)|BITS_MASK(RX_BIST,0x8,18,4)|BITS_MASK(RX_BIST,0x0,0,3)
[rfeSwOcOtp_otpRegAddr_2C4_e] = 0x41dfe85, // BITS_MASK(CHIRPPLL,0x7,18,4)|BITS_MASK(CHIRPPLL,0x1f,12,6)|BITS_MASK(CHIRPPLL,0x3a,6,6)|BITS_MASK(CHIRPPLL,0x5,0,6)|BITS_MASK(CHIRPPLL,0x10,22,6)
[rfeSwOcOtp_otpRegAddr_2C8_e] = 0xfc74565, // BITS_MASK(CHIRPPLL,0xf,24,7)|BITS_MASK(CHIRPPLL,0x31,18,6)|BITS_MASK(CHIRPPLL,0x34,12,6)|BITS_MASK(CHIRPPLL,0x15,6,6)|BITS_MASK(CHIRPPLL,0x25,0,6)
[rfeSwOcOtp_otpRegAddr_2CC_e] = 0x2710481c, // BITS_MASK(CHIRPPLL,0x481c,0,16)|BITS_MASK(CHIRPPLL,0x2710,16,16)
[rfeSwOcOtp_otpRegAddr_2D0_e] = 0x9c41c20, // BITS_MASK(CHIRPPLL,0x9c4,16,16)|BITS_MASK(CHIRPPLL,0x1c20,0,16)
[rfeSwOcOtp_otpRegAddr_2D4_e] = 0x1861f40, // BITS_MASK(CHIRPPLL,0x186,16,9)|BITS_MASK(CHIRPPLL,0x1f40,0,16)
[rfeSwOcOtp_otpRegAddr_2D8_e] = 0x97bdef, // BITS_MASK(ATB,0x9,20,4)|BITS_MASK(ATB,0xf,15,5)|BITS_MASK(ATB,0xf,10,5)|BITS_MASK(ATB,0xf,5,5)|BITS_MASK(ATB,0xf,0,5)|BITS_MASK(ATB,0x0,24,2)|BITS_MASK(ATB,0x0,26,2)|BITS_MASK(ATB,0x0,28,2)|BITS_MASK(ATB,0x0,30,2)
[rfeSwOcOtp_otpRegAddr_2DC_e] = 0x1c, // BITS_MASK(ATB,0x0,24,8)|BITS_MASK(ATB,0x0,19,5)|BITS_MASK(ATB,0x0,11,8)|BITS_MASK(ATB,0x0,6,5)|BITS_MASK(ATB,0x3,3,3)|BITS_MASK(ATB,0x4,0,3)

## Slide 12
[rfeSwOcOtp_otpRegAddr_2E0_e] = 0x1c, // BITS_MASK(ATB,0x0,24,8)|BITS_MASK(ATB,0x0,19,5)|BITS_MASK(ATB,0x0,11,8)|BITS_MASK(ATB,0x0,6,5)|BITS_MASK(ATB,0x3,3,3)|BITS_MASK(ATB,0x4,0,3)
[rfeSwOcOtp_otpRegAddr_2E4_e] = 0x9084210, // BITS_MASK(GLOBAL_BIAS,0x4,25,3)|BITS_MASK(GLOBAL_BIAS,0x10,20,5)|BITS_MASK(GLOBAL_BIAS,0x10,15,5)|BITS_MASK(GLOBAL_BIAS,0x10,10,5)|BITS_MASK(GLOBAL_BIAS,0x10,5,5)|BITS_MASK(GLOBAL_BIAS,0x10,0,5)
[rfeSwOcOtp_otpRegAddr_2E8_e] = 0x21084210, // BITS_MASK(GLOBAL_BIAS,0x10,25,5)|BITS_MASK(GLOBAL_BIAS,0x10,20,5)|BITS_MASK(GLOBAL_BIAS,0x10,15,5)|BITS_MASK(GLOBAL_BIAS,0x10,10,5)|BITS_MASK(GLOBAL_BIAS,0x10,5,5)|BITS_MASK(GLOBAL_BIAS,0x10,0,5)
[rfeSwOcOtp_otpRegAddr_2EC_e] = 0x49212490, // BITS_MASK(GLOBAL_BIAS,0x4,25,3)|BITS_MASK(GLOBAL_BIAS,0x4,22,3)|BITS_MASK(GLOBAL_BIAS,0x10,17,5)|BITS_MASK(GLOBAL_BIAS,0x4,14,3)|BITS_MASK(GLOBAL_BIAS,0x4,11,3)|BITS_MASK(GLOBAL_BIAS,0x4,8,3)|BITS_MASK(GLOBAL_BIAS,0x4,5,3)|BITS_MASK(GLOBAL_BIAS,0x10,0,5)|BITS_MASK(GLOBAL_BIAS,0x4,28,3)
[rfeSwOcOtp_otpRegAddr_2F0_e] = 0x21242124, // BITS_MASK(GLOBAL_BIAS,0x10,25,5)|BITS_MASK(GLOBAL_BIAS,0x4,22,3)|BITS_MASK(GLOBAL_BIAS,0x4,19,3)|BITS_MASK(GLOBAL_BIAS,0x10,14,5)|BITS_MASK(GLOBAL_BIAS,0x10,9,5)|BITS_MASK(GLOBAL_BIAS,0x4,6,3)|BITS_MASK(GLOBAL_BIAS,0x4,3,3)|BITS_MASK(GLOBAL_BIAS,0x4,0,3)
[rfeSwOcOtp_otpRegAddr_2F4_e] = 0x49084210, // BITS_MASK(GLOBAL_BIAS,0x4,28,3)|BITS_MASK(GLOBAL_BIAS,0x4,25,3)|BITS_MASK(GLOBAL_BIAS,0x10,20,5)|BITS_MASK(GLOBAL_BIAS,0x10,15,5)|BITS_MASK(GLOBAL_BIAS,0x10,10,5)|BITS_MASK(GLOBAL_BIAS,0x10,5,5)|BITS_MASK(GLOBAL_BIAS,0x10,0,5)
[rfeSwOcOtp_otpRegAddr_2F8_e] = 0x21084210, // BITS_MASK(GLOBAL_BIAS,0x10,25,5)|BITS_MASK(GLOBAL_BIAS,0x10,20,5)|BITS_MASK(GLOBAL_BIAS,0x10,15,5)|BITS_MASK(GLOBAL_BIAS,0x10,10,5)|BITS_MASK(GLOBAL_BIAS,0x10,5,5)|BITS_MASK(GLOBAL_BIAS,0x10,0,5)
[rfeSwOcOtp_otpRegAddr_2FC_e] = 0x42124924, // BITS_MASK(GLOBAL_BIAS,0x10,26,5)|BITS_MASK(GLOBAL_BIAS,0x10,21,5)|BITS_MASK(GLOBAL_BIAS,0x4,18,3)|BITS_MASK(GLOBAL_BIAS,0x4,15,3)|BITS_MASK(GLOBAL_BIAS,0x4,12,3)|BITS_MASK(GLOBAL_BIAS,0x4,9,3)|BITS_MASK(GLOBAL_BIAS,0x4,6,3)|BITS_MASK(GLOBAL_BIAS,0x4,3,3)|BITS_MASK(GLOBAL_BIAS,0x4,0,3)
[rfeSwOcOtp_otpRegAddr_300_e] = 0x48820, // BITS_MASK(GLOBAL_BIAS,0x4,16,3)|BITS_MASK(GLOBAL_BIAS,0x8,12,4)|BITS_MASK(GLOBAL_BIAS,0x20,6,6)|BITS_MASK(GLOBAL_BIAS,0x20,0,6)
[rfeSwOcOtp_otpRegAddr_310_e] = 0x0, // BITS_MASK(TX_1,0x0,22,10)|BITS_MASK(TX_1,0x0,16,6)|BITS_MASK(TX_1,0x0,6,10)|BITS_MASK(TX_1,0x0,0,6)
[rfeSwOcOtp_otpRegAddr_314_e] = 0x0, // BITS_MASK(TX_2,0x0,22,10)|BITS_MASK(TX_2,0x0,16,6)|BITS_MASK(TX_2,0x0,6,10)|BITS_MASK(TX_2,0x0,0,6)
[rfeSwOcOtp_otpRegAddr_318_e] = 0x0, // BITS_MASK(TX_3,0x0,22,10)|BITS_MASK(TX_3,0x0,16,6)|BITS_MASK(TX_3,0x0,6,10)|BITS_MASK(TX_3,0x0,0,6)
[rfeSwOcOtp_otpRegAddr_31C_e] = 0x0, // BITS_MASK(TX_4,0x0,22,10)|BITS_MASK(TX_4,0x0,16,6)|BITS_MASK(TX_4,0x0,6,10)|BITS_MASK(TX_4,0x0,0,6)
[rfeSwOcOtp_otpRegAddr_320_e] = 0x71c71c, // BITS_MASK(TX_1,0x0,24,1)|BITS_MASK(TX_1,0x0,25,1)|BITS_MASK(TX_2,0x0,26,1)|BITS_MASK(TX_2,0x0,27,1)|BITS_MASK(TX_3,0x0,28,1)|BITS_MASK(TX_3,0x0,29,1)|BITS_MASK(TX_4,0x0,30,1)|BITS_MASK(TX_4,0x0,31,1)|BITS_MASK(TX_1,0x3,21,3)|BITS_MASK(TX_1,0x4,18,3)|BITS_MASK(TX_2,0x3,15,3)|BITS_MASK(TX_2,0x4,12,3)|BITS_MASK(TX_3,0x3,9,3)|BITS_MASK(TX_3,0x4,6,3)|BITS_MASK(TX_4,0x3,3,3)|BITS_MASK(TX_4,0x4,0,3)
[rfeSwOcOtp_otpRegAddr_338_e] = 0xf180000, // BITS_MASK(ATB,0x3,19,5)|BITS_MASK(ATB,0x3,19,5)|BITS_MASK(RFE,0xf,24,8)
[rfeSwOcOtp_otpRegAddr_33C_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)
[rfeSwOcOtp_otpRegAddr_340_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)
[rfeSwOcOtp_otpRegAddr_344_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)
[rfeSwOcOtp_otpRegAddr_348_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)
[rfeSwOcOtp_otpRegAddr_34C_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)
[rfeSwOcOtp_otpRegAddr_350_e] = 0xf, // BITS_MASK(RFE,0xf,0,32)